## Slide 1
Combinational Logic Design
An Overview
Digital Electronics

## Slide 2: Combinational Logic
This presentation will
Review the logic symbol, logic expression, and truth table for the:
  AND gate
  OR gate
  INVERTER gate
Introduce the design for a simple combinational logic circuit.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: General Form for All Logic Gates
X | Y | Z
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?
X
Y
Z = X  Y
Note: There’s no such thing as a smiley face gate.
Logic Symbol
Inputs
Logic Expression
Output
Lists the output condition for all
possible input combinations.
Truth Table
Notes: This slide identifies the three forms that can be used to represent a logic gate. The three forms are (i) the logic symbol, (ii) the logic expression, and (iii) the truth table.

## Slide 4: AND Gates
X
Y
Three ways to write the AND symbol
X | Y | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Z is TRUE whenever X AND Y are TRUE
Notes: The basics of an AND gate

## Slide 5: OR Gates
X
Y
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Z is TRUE whenever X OR Y are TRUE
Notes: The basics of an OR gate

## Slide 6: INVERTER Gates
X
X | Z
0 | 1
1 | 0
Z is TRUE whenever X is NOT TRUE
The inverter is sometimes called the NOT gate.
The NOT symbol or bar
Notes: The basics of an INVERTER gate

## Slide 7: AOI Logic
Combinational logic designs implemented with AND gates, OR gates, and INVERTER gates are referred to as AOI designs.
AOI Logic is just one type of combinational logic. Unit 2 of this course will spend a significant amount of time exploring other forms of combinational logic and their applications.
The purpose of this introduction is to provide a basis of understanding for the combinational logic subsection of the Board Game Counter design.
AND
OR
INVERT
Notes: A brief explanation of AOI logic and why it is being introduced at this point.

## Slide 8: Example: Combinational Logic Design
This design controls the safety buzzer in a car and is designed to the following specifications:
  The BUZZER is ON whenever the DOOR is OPEN OR when the KEY is in the IGNITION AND the SEAT BELT is NOT BUCKELED.
Notes: Specifications for a simple combinational logic design

## Slide 9: Example: Truth Table
Car Buzzer – Truth Table |  |  | 
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Seat Belt
Key
Door
Buzzer
0 : Door is NOT Open
1 : Door is Open
0 : Key is NOT in the Ignition
1 : Key is in the Ignition
0 : Buzzer is OFF
1 : Buzzer is ON
0 : Seat Belt is NOT Buckled
1 : Seat Belt is Buckled
The BUZZER is ON whenever
  the DOOR is OPEN
  OR
  the KEY is in the IGNITION AND the SEAT BELT is NOT buckled.
Notes: Car buzzer truth table -- Explain how the design specification is mapped to the truth table.

## Slide 10: Example: Circuit Design
NOT buckled
in the IGNITION
  is OPEN
AND
OR
Notes: Car buzzer circuit diagram or schematic. Many students will be able to design this simple example directly from the word problem; thus, they may not need to create the truth table.

## Slide 11: Example: Functional Test (1 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 0 – 0 – 0.

## Slide 12: Example: Functional Test (2 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 0 – 0 – 1.

## Slide 13: Example: Functional Test (3 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 0 – 1 – 0.

## Slide 14: Example: Functional Test (4 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 0 – 1 – 1.

## Slide 15: Example: Functional Test (5 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 1 – 0 – 0.

## Slide 16: Example: Functional Test (6 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 1 – 0 – 1.

## Slide 17: Example: Functional Test (7 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 1 – 1 – 0.

## Slide 18: Example: Functional Test (8 of 8)
Seat Belt | Key | Door | Buzzer
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Logic ‘0’
Logic ‘1’
Notes: Step-by-step analysis (functional test) of the car buzzer design. This is for input combination 1 – 1 – 1.

## Slide 19: Example: IC Component View
1
2
3
2
1
3
2
1
Notes: This slide shows how the gates are actually part of integrated circuits. This connection diagram were taken directly from the manufacturer’s datasheet for the three components.

## Slide 20: Example Using LEDs
LED – Light Emitting Diode
LED
Notes: Shown is the complete logic diagram for the car buzzer design with light emitting diodes (LED) for the output.

## Slide 21: LED – Light Emitting Diode
To Turn an LED ON
The ANODE must be at a higher voltage potential (1.5v) than the CATHODE.
The amount of current flowing through the LED will determine how bright it is.
The amount of current is controlled by a series resistor. (not shown)
CATHODE (‒)
(+) ANODE
← Current Flow
LED
Notes: Brief explanation of how a light emitting diode (LED) works.

## Slide 22: LED Examples
Logic 1
 5 volts
CATHODE
ANODE
CATHODE
ANODE
Logic 0
 0 volts
The 180 resistor controls the current that flows through the LED. This in turn controls its brightness.
The ANODE is NOT at a higher voltage potential than the CATHODE; the LED is OFF.
The ANODE is at a higher voltage potential than the CATHODE; the LED is ON.
LED
LED
Logic 0
 0 volts
Notes: Explanation of one LED that is ON and another that is OFF.

## Slide 23: Combinational & Sequential Logic
Combinational
Logic Gates
Inputs
Outputs
.
.
.
.
.
.
Combinational
Logic Gates
.
.
Inputs
Outputs
Memory Elements
(Flip-Flops)
.
.
Clock
Combinational
Logic
Sequential
Logic
Notes: This slide defines combinational & sequential logic. Combinational Logic has one or more inputs and one or more outputs. The outputs are a function of the present value of the inputs.
Sequential Logic can also have one or more inputs and one or more outputs. However, with sequential logic, the outputs are a function of both the present value of the inputs and also the previous output values. Thus, sequential logic requires memory to store previous output values.